## Slide 1: Machine Learning Ensemble for Flood Susceptibility Mapping in Garhwal Himalaya
Raj Amritam*, Nidhi Rawat
Department of Environmental Science, DBS Global University, Dehradun
International Conference on Geospatial Technologies
for Disaster Management (ICGTDM-2025)
IIT Roorkee, March 2025

## Slide 2: Background & Problem Statement
• India: 40M hectares flood-prone, INR 25,000 Cr annual damage
• Indian Himalayan Region: Extreme precipitation + steep terrain + young geology
• 2013 Kedarnath: 5,700+ deaths - worst single flood event
• AI/ML methods revolutionizing flood susceptibility mapping globally
• GAP: No ensemble ML framework validated for Garhwal Himalaya conditions
• Need: High-accuracy flood maps for NbS planning & disaster management

## Slide 3: Research Objectives
1. Develop ensemble ML model (Random Forest + XGBoost) for flood
susceptibility mapping in Alaknanda-Mandakini watershed
2. Identify key geo-environmental conditioning factors
3. Compare ensemble performance against individual models
(RF, XGBoost, SVM, ANN)
4. Validate through spatial cross-validation and field verification

## Slide 4: Study Area: Alaknanda-Mandakini Watershed
• Location: Garhwal Himalaya, Uttarakhand, India
• Area: 12,511 km² | Elevation: 475-7,816 m
• Rainfall: 1,200-2,800 mm (75-85% monsoonal)
• Major events: 2013, 2021, 2023 floods
• Drainage density: 3.42-3.87 km/km²
• LULC: 32% forest, 15% scrubland, 12% agriculture
• Geological complexity: Lesser + Higher + Tethys Himalaya

## Slide 5: Methodology
DATA:
• Flood inventory: 347 GPS-documented flood points
• 14 conditioning factors (DEM, slope, TWI, rainfall, LULC, etc.)
• Multicollinearity check: All VIF < 5
MODELS:
• Random Forest: 500 trees, sqrt features, 5-fold CV
• XGBoost: 300 trees, depth=6, lr=0.1, Bayesian optimization
• Ensemble: Weighted voting (RF:0.45 + XGB:0.55)
• Comparison: SVM (RBF), ANN (MLP)
VALIDATION: AUC-ROC, Accuracy, F1, Kappa, 10-fold spatial CV

## Slide 6: Results: Model Performance Comparison
┌─────────────────┬────────┬──────────┬─────────┬────────┐
│ Model │ AUC │ Accuracy │ F1 │ Kappa │
├─────────────────┼────────┼──────────┼─────────┼────────┤
│ Random Forest │ 0.921 │ 87.5% │ 0.87 │ 0.75 │
│ XGBoost │ 0.938 │ 89.4% │ 0.89 │ 0.79 │
│ SVM (RBF) │ 0.892 │ 84.1% │ 0.84 │ 0.68 │
│ ANN (MLP) │ 0.903 │ 85.6% │ 0.85 │ 0.71 │
│ RF+XGB Ensemble │ 0.946 │ 91.3% │ 0.91 │ 0.83 │
└─────────────────┴────────┴──────────┴─────────┴────────┘
★ Ensemble outperforms all individual models across ALL metrics

## Slide 7: Results: Feature Importance (Top 7)
1. Distance to River .............. 0.187 (18.7%)
2. Slope Gradient ................. 0.156 (15.6%)
3. Topographic Wetness Index ...... 0.134 (13.4%)
4. Rainfall Intensity ............. 0.112 (11.2%)
5. Elevation ...................... 0.098 (9.8%)
6. LULC Class .................... 0.084 (8.4%)
7. Drainage Density ............... 0.072 (7.2%)
→ Top 5 factors account for 68.7% of total importance
→ NDVI (vegetation) at rank 8 supports NbS rationale

## Slide 8: Results: Flood Susceptibility Zone Distribution
Zone Distribution (% area):
Alaknanda Mandakini
Very High: 8.2% 11.4%
High: 14.6% 18.3%
Moderate: 22.8% 24.1%
Low: 31.2% 27.8%
Very Low: 23.2% 18.4%
→ Mandakini: 29.7% in High/Very High (vs 22.8% Alaknanda)
→ Consistent with 2013 Kedarnath disaster epicenter location

## Slide 9: Conclusions & Implications
KEY FINDINGS:
✓ RF+XGBoost ensemble: AUC=0.946, Accuracy=91.3%
✓ Distance to river is dominant predictor (18.7%)
✓ Mandakini more vulnerable than Alaknanda (29.7% vs 22.8% high zones)
✓ Vegetation (NDVI) has measurable influence → supports NbS
IMPLICATIONS:
• Provides foundation for NbS site selection framework
• Enables rapid flood hazard mapping for ungauged basins
• Transferable to other Himalayan watersheds (validated: AUC=0.87)
• Supports evidence-based disaster management planning

## Slide 10: Thank You!
Contact:
Raj Amritam
raj.amritam@dbsgu.ac.in
Department of Environmental Science
DBS Global University, Dehradun
Acknowledgements:
• SDMA Uttarakhand (flood data)
• IMD & CWC (meteorological/hydrological data)
• DBS Global University (infrastructure)