## Slide 1: Nature-Based Solutions vs Grey Infrastructure: A Cost-Benefit Analysis for Himalayan Flood Management
Raj Amritam*, Nidhi Rawat
Department of Environmental Science, DBS Global University, Dehradun
National Conference on Climate Change Adaptation
and Disaster Resilience (NCCADR-2025)
TERI University, New Delhi, June 2025

## Slide 2: The Flood Management Challenge in India
SCALE OF CRISIS:
• 40 million hectares flood-prone | 42% of disaster deaths
• INR 25,000 Crore annual flood damage
• IHR: 2013 Kedarnath (5,700 deaths), 2021 Chamoli, 2023 HP floods
GREY INFRASTRUCTURE LIMITATIONS:
• Capital-intensive: INR 2-15 Cr/km for embankments
• Limited design life: 25-50 years
• Ecological destruction: riparian habitat loss
• Transfers risk downstream
• FAILS when exceeded: catastrophic failure mode
QUESTION: Can NbS provide BETTER flood protection at LOWER cost?

## Slide 3: Nature-Based Solutions for Flood Mitigation
DEFINITION (IUCN, 2016): Actions to protect, manage, and restore
ecosystems that address societal challenges while providing
biodiversity benefits.
NbS TYPES FOR FLOOD MANAGEMENT:
• Riparian Buffer Restoration (30-100m riverbank forests)
• Wetland Rehabilitation (floodplain storage)
• Slope Afforestation (interception + infiltration)
• Check Dam Cascades (headwater attenuation)
• Terrace Enhancement (runoff reduction)
MECHANISMS: Intercept rainfall → Increase infiltration →
Store water → Slow flow → Attenuate peaks

## Slide 4: Study Design & Methodology
STUDY AREA: Alaknanda-Mandakini watershed (12,511 km²)
APPROACH: Scenario-based hydrological modeling
• Baseline: No intervention (current state)
• NbS: 47 optimal sites (231 km²) from AI-GIS MCDA
• Grey: Equivalent investment in engineered structures
MODELS: HEC-HMS (event) + SWAT (continuous)
• Return periods: 10, 25, 50, 100 years
• Climate: Current + RCP 4.5 + RCP 8.5 (2050)
ECONOMICS: 50-year CBA, 8% discount rate
• Benefits: Avoided damage + Co-benefits

## Slide 5: Results: Peak Discharge Reduction
AT RUDRAPRAYAG (Mandakini outlet):
Return Period NbS Reduction Grey Reduction Winner
──────────── ───────────── ────────────── ──────
10-year -31.7% -20.0% NbS ✓
25-year -29.0% -20.0% NbS ✓
50-year -25.1% -20.0% NbS ✓
100-year -22.5% -14.0% NbS ✓
FLOOD EXTENT (100-yr RP):
• Baseline: 48.2 km²
• NbS: 28.4 km² (-41.1%)
• Grey: 35.6 km² (-26.1%)
→ NbS reduces flood area 57% MORE than grey infrastructure!

## Slide 6: Results: Cost-Benefit Analysis (50-year horizon)
NbS (47 sites) Grey Infrastructure
────────────── ──────────────────
Capital Cost INR 24.5 Cr INR 38.2 Cr
Annual Maintenance INR 1.2 Cr/yr INR 3.8 Cr/yr
Design Life 50-100+ years 25-50 years
────────────────────────────────────────────────────────
Avoided Damage INR 18.4 Cr/yr INR 12.7 Cr/yr
Co-benefits INR 5.8 Cr/yr INR 0.3 Cr/yr
────────────────────────────────────────────────────────
BCR 4.2 : 1 1.8 : 1
NPV (@ 8%) INR 85.3 Cr INR 28.6 Cr
IRR 34% 14%
★ NbS: 2.3x BETTER return on investment!

## Slide 7: NbS Co-Benefits: INR 5.8 Crore/year
BREAKDOWN:
Carbon Sequestration ......... INR 2.1 Cr/yr
(14,000 tCO2e/yr × INR 1,500/tCO2e)
Biodiversity Habitat ......... INR 1.4 Cr/yr
(231 km² restored habitat, species recovery)
Water Quality Improvement .... INR 1.2 Cr/yr
(Reduced sediment load, drinking water protection)
Livelihood Benefits .......... INR 1.1 Cr/yr
(NTFP, ecotourism, fodder, sustainable harvest)
→ Grey infrastructure co-benefits: nearly ZERO (INR 0.3 Cr)

## Slide 8: Results: Performance Under Climate Change (2050)
NbS RESILIENCE:
Scenario NbS Efficacy Retained Still Better than Grey?
────────────── ───────────────────── ─────────────────────
RCP 4.5 (moderate) 73% YES (NbS: 16-23%)
RCP 8.5 (severe) 62% EQUAL (NbS: 14-20%)
WHY NbS IS MORE RESILIENT:
• Self-maintaining: ecosystems adapt to new conditions
• No catastrophic failure mode (unlike dam overtopping)
• Growing effectiveness as forests mature (decades)
• Additional carbon sequestration under higher CO2
Grey infrastructure DEGRADES faster under climate change
(accelerated erosion, higher maintenance, earlier replacement)

## Slide 9: Policy Recommendations
BASED ON EVIDENCE:
1. ALLOCATE minimum 20% of flood management budget to NbS
(Currently: <2% nationally)
2. INTEGRATE NbS into State Disaster Management Plans
as mandatory alongside grey infrastructure
3. ADOPT Hydro-Spatial Modeling Framework (HSMF) as
standard assessment tool across IHR states
4. ESTABLISH Payment for Ecosystem Services (PES)
for NbS maintenance from downstream beneficiaries
5. MANDATE NbS-equivalence analysis in EIAs for
all new grey flood control projects

## Slide 10: Conclusions
SUMMARY:
✓ NbS reduces floods 22-34% at 36% LOWER cost than grey
✓ BCR 4.2:1 (NbS) vs 1.8:1 (Grey) — NbS is 2.3x better
✓ Co-benefits worth INR 5.8 Cr/yr (grey: nearly zero)
✓ NbS maintains performance under climate change
✓ 71-82% community acceptance
✓ Framework transferable (60% less data for new basins)
BOTTOM LINE:
NbS is scientifically superior, economically viable,
and community-supported for Himalayan flood management.
It's time to shift from GREY to GREEN.

## Slide 11: Thank You! Questions?
Raj Amritam
raj.amritam@dbsgu.ac.in
Department of Environmental Science
DBS Global University, Dehradun
Publications:
1. Amritam & Rawat (2025) J. Hydrology, 632, 130845
2. Amritam & Rawat (2025) Sci. Total Environ., 912, 169234
Acknowledgements: SDMA, IMD, CWC, DBS Global University